## Slide 1: Ikazuchi Zero™ PTCA Pre-Dilatation Catheter
Attribute | Description | 
Nominal Pressure (NP) ¦ Rated Pressure (RBP) | 6 atm (NP) | 14 atm (RBP)
Tip OD (tip entry profile) | 0.40 mm | 
Balloon Compliance | Balloon diameter (mm) | % Growth (6 atm to 14 atm)
 | 1.00 1.50 2.00 2.25 2.50 2.75 3.00 | 9.00% 7.33% 8.00% 8.44% 8.80% 8.73% 8.33%
Compatible Max Guidewire OD | 0.014” | 
Guide Catheter Compatibility | 5 F | 
Tip material (length) | Pebax (4.0m) | 
Effective Length | 146 cm | 
Proximal Shaft Diameter | 2F (ø1.0, ø3.0 mm); 1.9F (ø1.5 - ø2.75 mm) | 
Distal Shaft Diameter | 2.5F (ø1.0, ø3.0 mm), 2.3F (ø1.5 - ø2.75 mm) | 
Shelf Life | 3 years | 
Coating | TR2 Coat Hydrophilic | 
Sterilization Process Used | EtO | 
# of Radiopaque Markers | 1: ø1.0m - ø1.5mm; 2: Over ø2.0mm | 
Balloon Wrapping | 2-fold: ø1.0mm - ø1.5mm; 3-fold: Over ø2.0mm | 
Primary Crossing Profile | 0.585 mm (ø1.0 mm) 0.838 mm (ø3.0 mm) | 
Accessory Device | Flushing Needle + Re-wrapping tool | 
 |  | Balloon Lengths |  |  | 
 |  | 6 mm | 10 mm | 15 mm | 20 mm
Balloon Diameters (mm) | 1.00 | ZE-6-100P |  |  | 
 | 1.50 |  | ZE-10-150 | ZE-15-150 | 
 | 2.00 |  | ZE-10-200 | ZE-15-200 | ZE-20-200
 | 2.25 |  | ZE-10-225 | ZE-15-225 | ZE-20-225
 | 2.50 |  | ZE-10-250 | ZE-15-250 | ZE-20-250
 | 2.75 |  | ZE-10-275 | ZE-15-275 | 
 | 3.00 |  | ZE-10-300 | ZE-15-300 | ZE-20-300
This presentation is intended for Healthcare Professionals in EMEA only. Prior to use, refer to the instruction for use supplied with this device for indications, contraindications, side effects, suggested procedure, warnings and precautions. Ikazuchi Zero & RAIDEN3 are manufactured by Kaneka and distributed by Cordis. The third party trademarks used herein are trademarks of their respective owners. Please contact your Cordis representative for product availability in your country. WARNINGS: STERILE product, to be for one-time use only. The inflated diameter of the balloon should correspond to the diameter of the vessel for treatment. CORDIS and Cordis LOGO are trademarks or registered trademarks of Cardinal Health. All other marks are the property of their respective owners. © 2017 Cardinal Health. All Rights Reserved. EU2071 02/17

## Slide 2: RAIDEN3™ PTCA Post-Dilatation Catheter
 |  | Balloon Length |  |  | Balloon Lengths |  | 
 |  | 8 mm |  |  | 10 mm | 15 mm | 20 mm
Balloon Diameters (mm) | 1.50 | RD3-8-150 | Balloon Diameters (mm) | 2.00 | RD3-10-200 | RD3-15-200 | 
 | 1.75 | RD3-8-175 |  | 2.25 | RD3-10-225 | RD3-15-225 | 
 |  |  |  | 2.50 | RD3-10-250 | RD3-15-250 | RD3-20-250
 |  |  |  | 2.75 | RD3-10-275 | RD3-15-275 | RD3-20-275
 |  |  |  | 3.00 | RD3-10-300 | RD3-15-300 | RD3-20-300
 |  |  |  | 3.25 | RD3-10-325 | RD3-15-325 | RD3-20-325
 |  |  |  | 3.50 | RD3-10-350 | RD3-15-350 | RD3-20-350
 |  |  |  | 3.75 | RD3-10-375 | RD3-15-375 | RD3-20-375
 |  |  |  | 4.00 | RD3-10-400 | RD3-15-400 | RD3-20-400
 |  |  |  | 4.25 | RD3-10-425 | RD3-15-425 | 
 |  |  |  | 4.50 | RD3-10-450 | RD3-15-450 | 
Attribute | Description |  |  | 
Nominal (NP) ¦ Rated Pressure (RBP) | NP: 12 atm | RBP: 20 atm (ø1.5 – 2.00 mm, ø4.25 – 4.50 mm), 22atm (ø2.25 – 4.00 mm) |  | 
Tip OD (tip entry profile) | 0.43mm |  |  | 
Balloon Compliance | Balloon diameter (mm) |  | % Growth (NP to RBP) | 
 | 1.50 1.75 2.00 2.25 2.50 2.75 3.00 3.25 3.50 3.75 4.00 4.25 4.50 |  | 6.67% 6.86% 5.50% 7.56% 8.40% 8.00% 6.33% 6.15% 6.29% 6.40% 6.50% 5.18% 5.11% | 
Compatible Max Guidewire OD | 0.014” |  |  | 
Guide Catheter Compatibility | 5 F |  |  | 
Tip material (length) | Pebax (4.0m) |  |  | 
Effective Length | 146cm |  |  | 
Proximal ¦ Distal Shaft Diameter | 2.1F |  |  | 2.5 - 2.7F
Shelf Life | 3 years |  |  | 
Coating | TR2 Coat Hydrophilic |  |  | 
# of Radiopaque Markers | 1: ø1.5mm - ø1.75mm; 2: Over ø2.0mm |  |  | 
Balloon Wrapping | 2-fold: ø1.5mm - ø1.75mm; 3-fold: Over ø2.0mm |  |  | 
Primary Crossing Profile | 0.85 mm (ø3.0 mm) |  |  |