## Slide 1: Olympus Immersion Oil Type-F
Putting the finishing touch to UIS2

## Slide 2: Olympus Low Fluorescent Immersion Oil
Improvements
Enhanced contrast due to dramatically reduced autofluorescence
Better useability by increased viscosity
High dispersion accuracy because of tigthened production standard
Keeping the product advantages of
low toxicity
low chemical reactivity with plastics
low odour
low tendency to gum

## Slide 3: Minimised autofluorescence
Increased contrast due to increased S/N ratio
The new oil has just 1/10 of the autofluorescence of the current oil
Best performance in UV in comparison to immersion oil from competitors and same performance level in the B/G wavelength range
New oil
Old oil
UPLSAPO60x, U-MWU, same exposure time

## Slide 4: Comparison with competitor‘s products

## Slide 5: Immersion Oil Type-F specifications
 Limited durability
 Refractive Index: 1.518 at 23°C
 Abbe Number: 41 at 23°C
 Viscosity: 450 cSt (centiStokes, see notes)
Produced according to ISO standard 8036 (see notes)
Notes: ISO 8036:2006 describes the characteristics of immersion liquids used in microscopy. It classifies immersion liquids according to their field of application and specifies requirements and test methods for each type. Kinematic viscosity (Greek symbol: ν) has SI units (m2·s−1). The cgs physical unit for kinematic viscosity is the stokes (abbreviated S or St), named after George Gabriel Stokes.
  1 stokes = 100 centistokes (cSt) = 1 cm2·s−1 = 0.0001 m2·s−1.
  1 centistokes = 1 mm2/s

## Slide 6: Specifications in detail
Refractive index of 1.518 according to ISO standard
Coverslips produced according to ISO 8255-1 have a refractive index of 1.52. Objectives are standardised for this refractive index. The RI of 1.518 of the immersion oil prevents spherical aberrations induced by refractive index mismatches.
Abbe number v: 41according to ISO standard
The Abbe number expresses the dispersion (chromatic aberration) of an optical medium. Olympus UIS2 immersion optics is designed for medium with v = 41. The new oil is produced with mucher lower variation (v = 39.5 – 42.5) than the current oil (v = 38 – 45) hence reducing chromatic aberrations eventually caused by Abbe number mismatch.

## Slide 7: Specifications in detail
Viscosity 435 cSt (no ISO standard defined)
The current oil has a very low viscosity of 135 cSt. Problematic especially for inverted microscopy because excess oil drains of easily. The increased viscosity of the new oil minimizes such problems without negative effects for long time experiments. Incubation tests for two weeks at 40°C showed no cristallisation or gum effects.
Limited durability according to ISO standard
Date of expiry must be indicated to meet ISO standard
Deteroriration effects after date of expiry might be spherical and chromatic abberrations due to change in refractive index and Abbe number
15 months minimum durability ex stock Hamburg long term storage experiments are under way to find out if the expiry date can be elongated

## Slide 8: New immersion oil, practical note
Confocal and TIRF microscopy
Reduced immersion oil autofluoresence with almost no impact
Because the illuminated sample volume is small and the oil is not excited
High Abbe number fidelity assures stable chromatic abberation performance
Oil with Abbe numbers deviating from design figures would cause significant chromatic shifts

## Slide 9: Olympus Immersion Oil Type-F
Order information Immersion Oil Type-F
Art. Code N2673200, IMMOIL-F30CC
Replaces 035505, IMMERSION OIL 50CC
The current oil is continued for non-fluorescence observations
035503, IMMERSION OIL 500CC
035520, IMMERSION OIL 8CC
Discontinued size of current oil
035505, IMMERSION OIL 50CC
Remaining stock is currently sold off